- The basic wiring diagram

| Terminal name | Function description |
| --- | --- |
| RS+ | RS485 positive |
| RS- | RS485 negative |

- Communication parameters

PD group Communication parameters show

| PD.00 | Baud rate | The factory value | 0005 |
| --- | --- | --- | --- |
|  | setting range | units' digit:MODUBS Baud rate 0：300BPS 1：600BPS 2：1200BPS 3：2400BPS 4：4800BPS 5：9600BPS 6：19200BPS 7：38400BPS 8：57600BPS 9：115200BPS |

This parameter is used to set data transfer rate between the PC and inverter.Notice that setting the baud rate of upper machine and converter must agree, otherwise, the communication can't carry on.The faster the baud rate, the greater the communication.

| PD.01 | The data format | The factory value | 0 |
| --- | --- | --- | --- |
|  | setting range | 0：No check：The data format<8,N,2> 1：Even-parity：The data format<8,E,1> 2：Odd parity check：The data format<8,O,1> 3：No check：The data format<8-N-1> |

PC and data format set by the frequency converter must agree, otherwise, the communication can't carry on.

| PD.02 | The machine address | The factory value | 1 |
| --- | --- | --- | --- |
|  | setting range | 1~247，0 is the broadcast address |

When the machine address set to 0, namely for the broadcast address, realize PC broadcasting functions.The machine address has uniqueness (except the broadcast address), which is to achieve the basis of upper machine and inverter peer-to-peer communications.

| PD.03 | Response latency | The factory value | 2ms |
| --- | --- | --- | --- |
|  | setting range | 0~20ms |

Response latency: refers to the frequency converter data to accept the end up to a upper machine to send data in the middle of the interval of time.If the response time delay is less than the system processing time, the response time delay will be subject to system processing time, processing time, such as response time delay is longer than system after processing the data, the system will delay waiting, until the response delay time to up to a upper machine to send data.

| PD.04 | Communication timeout | The factory value | 0.0 s |
| --- | --- | --- | --- |
|  | setting range | 0.0 s（invalid） 0.1~60.0s |

When the function code is set to 0.0 s, communication timeout parameter is invalid.

When the function code set to valid values, if a communication and the interval time of the next communication beyond the communication timeout, system will be submitted to the communication failure error (CE).Usually, it is set into is invalid.If, in the continuous communication system parameter set the time, you can monitor the communication status.

| PD.05 | Communication protocol selection | The factory value | 0 |
| --- | --- | --- | --- |
|  | setting range | 0：Non standard Modbus protocol 1：The standard Modbus protocol |

PD.05=1：choose the standard Modbus protocol

PD.05=0：when reading command ,Returns number of bytes from the machine is a byte more than the standard Modbus protocol, detailed in this agreement 5 Communication data structures.

| PD.06 | Read the current resolution | The factory value | 1 |
| --- | --- | --- | --- |
|  | setting range | 0：0.01A 1：0.1A |

Used to determine the communication while reading the output current, current value of the output units.

3、Communication Protocol

NZ2000 series inverter provides RS232 / RS485 communication interface, and support the Modbus communication protocol. Users can be achieved by computing machine or PLC central control, through the communication protocol set frequency converter running commands, modify or read function code parameters, read the inverter working condition and fault information, etc.

3.1、The agreement content

The serial communication protocol defines the serial communication transmission of information content and format.Including: host polling or wide planting format;Host encoding method, the content includes: the function of the required action code, data transmission and error checking, etc.From the ring of machine should be used is the same structure, content including: action confirmation, return the data and error checking, etc.If there was an error in receiving information from a machine, or cannot achieve the requirements of the host, it will organize a fault feedback information in response to the host.

3.2、Application methods

Application mode converter with RS232 / RS485 bus access to the "from" single main PC/PLC control network.

3.3、Bus structure

（1） The interface way  RS232 / RS485 interface hardware

（2） Asynchronous serial  transmission mode, half-duplex transmission mode.At the same time the host and the only one to send data from the machine and the other can only receive data.Data in the process of serial asynchronous communication, the form of a message, a frame of a frame to send

（3）Topological structure from single host machine system.From the machine address set in the range of 1 ~ 247, 0 for broadcast communication address.In the network from the machine address must be unique.

3.4、Protocol Description

NZ2000 series inverter is a kind of asynchronous serial port communication protocol of master-slave Modbus communication protocol, the network has only one equipment (host) to establish agreement (called "query/command").Other equipment (machine) can only by providing data response of the main machine "query/command", or "query/command" according to the host to make the corresponding action.Host in this refers to the personal computer (PC), industrial control equipment or programmable logic controller (PLC), etc., from machine refers to NZ2000 inverter.The host can communicate to a separate from the machine, also can to all under a broadcast information from machine release.For access to the host alone "query/command", from the machine to return to a information (called response), for radio host information, from the machine without feedback response to the host.

3.5、Communications data structure

Communication data structure NZ2000 series frequency converter of the Modbus protocol communication data format is as follows: using the RTU mode, messages are sent at least begin with 3.5 characters pause time interval.

In network wave rate under varied characters of the time, this is the most easy to implement (below T1, T2, T3, T4).Transmission equipment is the first domain address.

The transmission character of you can use is the hex 0...9, A...F.Continuously detect network bus network facilities, including pause interval of time.When the first domain (domain) to receive, every equipment decoding to determine whether to own.After the last transmission character, a pause at least 3.5 characters time calibration for the end of the message.A new message can be started after the pause.

The entire message frame must be as a continuous flow of transmission.If the time frame to complete more than 1.5 characters before pause time, receiving equipment will refresh incomplete message and assume that the next byte is a new message the address of the domain.Likewise, if a new message in less than 3.5 characters of time and then a message before, receiving equipment will think it is a continuation of the previous message.This will result in an error, because in the final CRC field value can't be right.

RTU frame format:

| The frame header START | 3.5 characters |
| --- | --- |
| Slave address ADR | Communication address：1~247 |
| command code CMD | 03：Read the machine parameters；06：write the machine parameters |
| Date content DATA（N-1） | Information content：Function code parameter address, function code number of parameters, function code parameter values, etc |
| Data content DATA（N-2） |  |
| …… |  |
| Data content DATA 0 |  |
| high-order position of CRC CHK | estimated value： CRC value |
| low-order position of CRC CHK |  |
| END | 3.5 characters’time |

CMD（Command instruction）and DATA（the description of data word）command code：03H，read N word（Word）（Can read the most words of 12）For example,From the machine address of 01 inverter startup F105 continuous read for two consecutive values.
The host command information

| ADR | 01H |
| --- | --- |
| CMD | 03H |
| high-order position of the starting address | F1H |
| low-order position of the starting address | 05H |
| high-order position of register | 00H |
| low-order position of register | 02H |
| low-order position of CRC CHK | Wait to calculate the CRC CHK values |
| high-order position of CRC CHK |  |

In response to information from the  slave machine

Set PD.05 to 0：

| ADR | 01H |
| --- | --- |
| CMD | 03H |
| high-order position of bytes | 00H |
| low-order position of bytes | 04H |
| Data high-order position of F002H | 00H |
| Data low-order position of F002H | 00H |
| Data high-order position of F003H | 00H |
| Data low-order position of F003H | 01H |
| low-order position of CRC CHK | Wait to calculate the CRC CHK values |
| high-order position of CRC CHK |  |

Set PD.05 to 1:

| ADR | 01H |
| --- | --- |
| CMD | 03H |
| The number of bytes | 04H |
| Data high-order position of F002H | 00H |
| Data low-order position of F002H | 00H |
| Data high-order position of F003H | 00H |
| Data low-order position of F003H | 01H |
| low-order position of CRC CHK | Wait to calculate the CRC CHK values |
| high-order position of CRC CHK |  |

The command code：06H write a word（Word）For example,write 000（BB8H）to  slave machine.

Address 05H frequency converter’s F00AH address.

The host command information

| ADR | 05H |
| --- | --- |
| CMD | 06H |
| high-order position of data address | F0H |
| low-order position of data address | 0AH |
| high-order position of information content | 0BH |
| low-order position of information content | B8H |
| low-order position of CRC CHK | Wait to calculate the CRC CHK values |
| high-order position of CRC CHK |  |

In response to information from the slave machine

| ADR | 02H |
| --- | --- |
| CMD | 06H |
| high-order position of data address | F0H |
| low-order position of data address | 0AH |
| high-order position of information content | 13H |
| low-order position of information content | 88H |
| low-order position of CRC CHK | Wait to calculate the CRC CHK values |
| high-order position of CRC CHK |  |

Check way——CRC Check way：CRC（Cyclical Redundancy Check）use RTU frame format,The message includes error detection field based on the method of CRC .CRC domain test the  whole content of a message。CRC domain is two bytes，contains a 16-bit binary values.it is calculated by the transmission equipment, added to the message.receive messages the device recalculate.And compared with receives the CRC in the domain of value, if the two CRC value is not equal, then there is an error in transmission.

CRC is saved in 0xFFFF,Then call a process to continuous 8-bit bytes of the message and the values in the current register for processing.Only 8 bit data in each character of CRC is effective，Starting bit and stopping  bit and parity bits are invalid.

In the process of CRC,Each of the eight characters are separate and dissimilar or register contents（XOR）,The results move to the least significant bit direction, set the most significant bit   to 0. LSB is extracted to test，if set LSB to 1,Register and preset value dissimilarity or alone，if set LSB to 0, is not to.The whole process will repeat 8 times.when the last time ( the eighth time) is completed，next  8-bit bytes and separate and register under the current value of the alien or.The values in the final register，Is all bytes in the message is executed after the CRC value.

When CRC added to the messages .The low byte to join first and then high byte.CRC Simple function is as follows:

unsigned int crc_cal_value(unsigned char *data_value,unsigned char data_length)

{

int i;

unsigned int crc_value=0xffff;

while(data_length--)

{

crc_value^=*data_value++;

for(i=0;i<8;i++)

{

If(crc_value&0x0001)

crc_value=(crc_value>>1)^0xa001;

else

crc_value=crc_value>>1;

}

}

Return(crc_value);

}

Address definition of communication parameters

This part is the content of the communication, used to control the operation of the inverter, inverter status and related parameters setting.Read and write functional code parameter (some function code which can not be changed, only for the use of manufacturers or monitoring) : function code parameter address label rules:
By function block number and the label for the parameter address  representation  rules .High byte: F0~FF（P group）、A0~AF（C group）、70~7F（D group）low byte：00~FF

Such as：P3.12，The address is expressed as F30C； attention： PF group：Neither read the parameters, and do not change parameters;Group D group: only can read, do not change the parameters.

When some parameters in converter is in operation, do not change;Some parameters of the frequency converter in any state, cannot be changed;Change function code parameters, but also pay attention to the range of parameters, units, and related instructions.

In addition, because the EEPROM is stored frequently, the service life of the block can reduce the the  life of the block EPROM, so some function code under the mode of communication, do not need to be stored, just change the value of RAM.If it is P group of parameters, in order to realize the function, as long as putting this function code address high F into 0 can be achieved.If it is C group of parameters, in order to realize the function, as long as putting the  function code  the address of high A into 4 can be achieved.Corresponding function codes are shown as the following address: the high byte: 00 ~ 0F (P group), 40 ~ 4F(group B) low byte: 00 to FF.

Such as:

Function code P3.12 is not stored in the EEPROM,The address is expressed as 030C；Function code C0-05 is not stored in the EEPROM,The address is expressed as 4005； The address representation can only do writing RAM，can’t do reading action,when reading,it is invalid address. For all the parameters, can also use the command code 7H to implement this function.

Stopping/starting parameters:

| Parameter address | Parameter description |
| --- | --- |
| 1000 | Communication Setting value（-10000~10000）（decimal system） |
| 1001 | Operating frequency |
| 1002 | Bus voltage |
| 1003 | output voltage |
| 1004 | current output |
| 1005 | output power |
| 1006 | output torque |
| 1007 | running velocity |
| 1008 | S Input Flag |
| 1009 | M01 output Flag |
| 100A | FIV voltage |
| 100B | FIC voltage |
| 100C | Reserved |
| 100D | count value input |
| 100E | The length of the input |
| 100F | The load speed |
| 1010 | PID setting |
| 1011 | PID feedback |
| 1012 | PLC steps |
| 1013 | PULSE the input pulse frequency,unit 0.01kHz |
| 1014 | Reserved |
| 1015 | The remaining running time |
| 1016 | FIV before correction voltage |
| 1017 | FIC before correction voltage |
| 1018 | Reserved |
| 1019 | Linear velocity |
| 101A | the current access to electricity time |
| 101B | the current running time |
| 101C | PULSE input pulse frequency,unit 1Hz |
| 101D | Communication Setting value |
| 101E | Reserved |
| 101F | The main frequency X show |
| 1020 | Auxiliary frequency Y show |

Attention：

Communication setting value is relative percentage, 10000 corresponds to 100.00% and -10000 corresponds to -100.00%.The frequency of dimensional data, the percentage is relative to the percentage of maximum frequency (P0.12);Counter rotating torque dimensional data, the percentage is P2.10.

Control command input to the converter:（write-only）

| The command word address | Command function |
| --- | --- |
| 2000 | 0001：Running forward |
|  | 0002：Reverse running |
|  | 0003：normal inching turning |
|  | 0004：Reversal point move |
|  | 0005：Free downtime |
|  | 0006：Slowing down |
|  | 0007：Failure reset |

Read the inverter state: (read-only)

| Status word address | Status word function |
| --- | --- |
| 3000 | 0001：Running forward |
|  | 0002：Reverse running |
|  | 0003：closing down |

Parameters lock password check: (if return for 8888H,it indicates that the password check through)

| Password address | The content of the input password |
| --- | --- |
| 1F00 | ***** |

| Command address | Command content |
| --- | --- |
| 2001 | BIT0：（reserve） BIT1：（reserve） BIT2：RA-RB-RC output control BIT3：YA-YB-YC output control BIT4：YO-R output control |

Analog output FOV control: (write-only)

| Command address | Command content |
| --- | --- |
| 2002 | 0～7FFF represent 0％～100％ |

Analog output control：（Reserved）

| Command address | Command content |
| --- | --- |
| 2003 | 0～7FFFrepresent 0％～100％ |

PULSE (PULSE) output control: (write -only)

| Command address | Command content |
| --- | --- |
| 2004 | 0～7FFFrepresent 0％～100％ |

Frequency converter fault description:

| Frequency converter fault address | Frequency converter fault information |
| --- | --- |
| 8000 | 0000：failure-free 0001：reserve 0002：Accelerate over current 0003：Slow down over current 0004：Constant speed over current 0005：Accelerate over the voltage 0006：Slow down over voltage 0007：Constant speed over voltage 0008：Buffer resistance overload fault 0009：Under-voltage fault 000A：The inverter overload 000B：Motor overload 000C：The input phase 000D：The output phase 000E：Module is overheating 000F：External fault 0010：Abnormal communication 0011：Abnormal contactor 0012：Current detection fault 0013：Motor tuning fault 0014：Encoder/PG card failure 0015：Abnormal parameters, reading and writing 0016：Inverter hardware failure 0017：Motor for short circuit fault 0018：reservation 0019：reservation 001A：Running time reached 001B: User-defined failure 1 001C: User-defined failure 2 001D: Accumulative power-on time reached 001E：Load becoming 0 001F：PID feedback lost during running 0028：With-wave current limit fault 0029：Motor switchover fault during running 002A: Too large speed deviation 002B： Motor over-speed 002D：Motor overheat 005A：Encoder line number setting error 005B：Don't connect the encoder 005C：Initial position fault 005E：Speed feedback error |

| Communication failures address | Fault feature description |
| --- | --- |
| 8001 | 0000：failure-free 0001：Password mistake 0002：The command code error 0003：CRC Checking error 0004：Invalid address 0005：Invalid parameter 0006：correcting parameter is invalid 0007：System is locked 0008：Block is EEPROM operation |

4、List of Function Parameters

If PP.00 is set to a non-zero number, parameter protection is enabled. You must enter the correct user password to enter the menu. To cancel the password protection function, enter with password and set PP.00 to 0.

Parameters menu the user customizes are not protected by password.Group P is the basic function parameters, Group D is to monitor the function parameters.

The symbols in the function code table are described as follows:

"☆": The parameter can be modified when the AC drive is in either stop or running state.

"★": The parameter cannot be modified when the AC drive is in the running state.

"●": The parameter is the actually measured value and cannot be modified.

"*" : The parameter is factory parameter and can be set only by the manufacturer.

Standard Function Parameters

| Function Code | Parameter Name | Setting Range | Command address | Property |
| --- | --- | --- | --- | --- |
| Group P0: Standard Function Parameters |
| P0.00 | G/P type display | 1：G type (constant torque load) 2：P type (variable torque load e.g. fan and pump) | F000 | ★ |
| P0.01 | Control mode selection | 0：Voltage/Frequency (V/F) control 1：Sensorless flux vector control (SFVC) | F001 | ★ |
| P0.02 | Command source selection | 0：Operation panel control (LED off） 1：Terminal control (LED on) 2：Communication control (LED linking) | F002 | ☆ |
| P0.03 | Frequency source selection | Unit's digit (Frequency source) 0：Main frequency source X 1：X and Y operation(operation relationship determined by ten's digit) 2：Switchover between X and Y 3：Switchover between X and "X and Y operation" 4：Switchover between Y and "X and Y operation" Ten's digit (X and Y operation) 0：X+Y 1：X-Y 2：Maximum 3：Minimum | F003 | ☆ |
| P0.04 | Main frequency source X selection | 0：Digital setting (P010 preset frequency, can modify the UP/DOWN, power lost don’t memory) 1：Digital setting (P010 preset frequency, can modify the UP/DOWN, power lost memory) 2：FIV 3：FIC 4：Reserved 5：Pulse setting（S3） 6：Multistage instruction 7：Simple PLC 8：PID 9：Communications given | F004 | ★ |
| P0.05 | Auxiliary frequency source Y selection | The same as P0.04 (Main frequency source X selection)） | F005 | ★ |
| P0.06 | Auxiliary frequency source superposition Y range selection | 0：Relative to the maximum frequency 1：Relative to the main frequency source X | F006 | ☆ |
| P0.07 | Auxiliary frequency source superposition Y range | 0%～150% | F007 | ☆ |
| P0.08 | Acceleration time 1 | 0.00s～65000s | F008 | ☆ |
| P0.09 | Deceleration time 1 | 0.00s～65000s | F009 | ☆ |
| P0.10 | Frequency preset | 0.00Hz～maximum frequency（P0.12） | F00A | ☆ |
| P0.11 | Rotation direction | 0：Same direction 1：Reverse direction | F00B | ☆ |
| P0.12 | Maximum frequency | 50.00Hz～320.00Hz | F00C | ★ |
| P0.13 | Upper limit frequency source | 0：P012 1：FIV 2：FIC 3：Reserved 4：PULSE settings 5：communication settings | F00D | ★ |
| P0.14 | Upper limit frequency | Frequency lower limit P0.16～Maximum frequency P0.12 | F00E | ☆ |
| P0.15 | Upper limit frequency offset | 0.00Hz～Maximum frequency P0.12 | F00F | ☆ |
| P0.16 | Frequency lower limit | 0.00Hz～Upper limit frequency P0.14 | F010 | ☆ |
| P0.17 | Carrier frequency | 1kHz～16.0kHz | F011 | ☆ |
| P0.18 | Carrier frequency adjustment with temperature | 0：No 1：Yes | F012 | ☆ |
| P0.19 | Acceleration/ Deceleration time unit | 0：1s 1：0.1s 2：0.01s | F013 | ★ |
| P0.21 | Frequency offset of auxiliary frequency source for X and Y operation | 0.00Hz～Maximum frequency P0.12 | F015 | ☆ |
| P0.22 | Frequency reference | 1:0.1Hz 2:0.01Hz | F016 | ★ |
| P0.23 | Retentive of digital setting frequency upon power | 0:Not retentive 1:Retentive | F017 | ☆ |
| P0.24 | Acceleration/ Deceleration time base frequency | 0:Maximum frequency（P0.12） 1:Set frequency 2:100Hz | F018 | ★ |
| P0.25 | Base frequency for UP/DOWN modification during running | 0：Running frequency 1：Set frequency | F019 | ★ |
| P0.26 | Binding command source to frequency source | Unit's digit:Binding operation panel command to frequency source 0:No binding 1:Frequency source by digital setting 2:FIV 3:FIC 4:Reserved 5:Pulse setting （S3） 6:Multi-reference 7:Simple PLC 8:PID 9:Communication setting Ten's digit:Binding terminal command to frequency source（0～9，same as unit's digit） Hundred's digit:Binding communication command to frequency source（0～9，same as unit's digit） | F01A | ☆ |
| P0.27 | Communication expansion card type | 0:Modbus communication card | F01B | ☆ |
| Group P1:Start/Stop Control |
| P1.00 | Start mode | 0：direct start 1：Rotational speed tracking restart 2：Pre-excited start (asynchronous motor) | F100 | ☆ |
| P1.01 | Rotational speed tracking mode | 0：From frequency at stop 1：From zero speed 2：From maximum frequency | F101 | ★ |
| P1.02 | Rotational speed tracking speed | 1～100 | F102 | ☆ |
| P1.03 | Startup frequency | 0.00Hz～10.00Hz | F103 | ☆ |
| P1.04 | Startup frequency holding time | 0.0s～100.0s | F104 | ★ |
| P1.05 | Startup DC braking current/Pre-excited current | 0%～100% | F105 | ★ |
| P1.06 | Startup DC braking time/Pre-excited time | 0.0s～100.0s | F106 | ★ |
| P1.07 | Acceleration/ Deceleration mode | 0：Linear acceleration/deceleration 1：S-curve acceleration/deceleration A 2：S-curve acceleration/deceleration B | F107 | ★ |
| P1.08 | Time proportion of S-curve start segment | 0.0%～（100.0%-P1.09） | F108 | ★ |
| P1.09 | Time proportion of S-curve end segment | 0.0%～（100.0%-P1.08） | F109 | ★ |
| P1.10 | Stop mode | 0：Decelerate to stop 1：Coast to stop | F10A | ☆ |
| P1.11 | Initial frequency of stop DC braking | 0.00Hz～maximum frequency | F10B | ☆ |
| P1.12 | Waiting time of stop DC braking | 0.0s～100.0s | F10C | ☆ |
| P1.13 | Stop DC braking current | 0%～100% | F10D | ☆ |
| P1.14 | Stop DC braking time | 0.0s～100.0s | F10E | ☆ |
| P1.15 | Brake use ratio | 0%～100% | F10F | ☆ |
| Group P2: Motor Parameter |
| P2.00 | Motor type selection | 0: Common asynchronous motor 1: Variable frequency asynchronous motor | F200 | ★ |
| P2.01 | Rated motor power | 0.1kW～1000.0kW | F201 | ★ |
| P2.02 | Rated motor voltage | 1V～2000V | F202 | ★ |
| P2.03 | Rated motor current | 0.01A～655.35A （AC drive power<=55kW） 0.1A～6553.5A （AC drive power>55kW） | F203 | ★ |
| P2.04 | Rated motor frequency | 0.01Hz～maximum frequency | F204 | ★ |
| P2.05 | Rated motor rotational speed | 1rpm～65535rpm | F205 | ★ |
| P2.06 | Stator resistance (asynchronous motor) | 0.001Ω～65.535Ω （AC drive power<=55kW） 0.0001Ω～6.5535Ω （AC drive power>55kW） | F206 | ★ |
| P2.07 | Rotor resistance (asynchronous motor) | 0.001Ω～65.535Ω （AC drive power<=55kW） 0.0001Ω～6.5535Ω （AC drive power>55kW） | F207 | ★ |
| P2.08 | Leakage inductive reactance (asynchronous motor) | 0.01mH～655.35mH （AC drive power<=55kW） 0.001mH～65.535mH （AC drive power>55kW） | F208 | ★ |
| P2.09 | No-load current (asynchronous motor) | 0.1mH～6553.5mH （AC drive power<=55kW） 0.01mH～655.35mH （AC drive power>55kW） | F209 | ★ |
| P2.10 | Stator resistance (synchronous motor) | 0.01A～P2.03（AC drive power<=55kW） 0.1A～P2.03（AC drive power>55kW） | F20A | ★ |
| P2.11-P2.36 Reserved |
| P2.37 | Auto-tuning selection | 0：No auto-tuning 1：Asynchronous motor static auto-tuning 2：Asynchronous motor complete auto-tuning | F225 | ★ |
| Group P3: Vector Control Parameters |
| P3.00 | Speed loop proportional gain 1 | 1～100 | F300 | ☆ |
| P3.01 | Speed loop integral time 1 | 0.01s～10.00s | F301 | ☆ |
| P3.02 | Switchover frequency 1 | 0.00～P3.05 | F302 | ☆ |
| P3.03 | Speed loop proportional gain 2 | 1～100 | F303 | ☆ |
| P3.04 | Speed loop integral time 2 | 0.01s～10.00s | F304 | ☆ |
| P3.05 | Switchover frequency 2 | P3.02～maximum output frequency | F305 | ☆ |
| P3.06 | Vector control slip gain | 50%～200% | F306 | ☆ |
| P3.07 | Time constant of speed loop filter | 0.000s～0.100s | F307 | ☆ |
| P3.08 | Vector control over-excitation gain | 0～200 | F308 | ☆ |
| P3.09 | Torque upper limit source in speed control mode | 0：P3.10 1：FIV 2：FIC 3：Reserved 4：Pulse setting 5：Communication setting 6：MIN（FIV,FIC） 7：MAX（FIV,FIC） | F309 | ☆ |
| P3.10 | digital setting of torque upper limit in speed control mode | 0.0%～200.0% | F30A | ☆ |
| P3.13 | Excitation adjustment proportional gain | 0～60000 | F30D | ☆ |
| P3.14 | Excitation adjustment integral gain | 0～60000 | F30E | ☆ |
| P3.15 | Torque adjustment proportional gain | 0～60000 | F30F | ☆ |
| P3.16 | Torque adjustment integral gain | 0～60000 | F310 | ☆ |
| P3.17 | Speed loop integral property | Unit's digit: integral separation 0：Disabled 1：Enabled | F311 | ☆ |
| P3.18 | Reserved |  | F312 |  |
| P3.19 | Reserved |  | F313 |  |
| P3.20 | Reserved |  | F314 |  |
| P3.21 | Reserved |  | F315 |  |
| P3.22 | Reserved |  | F316 |  |
| Group P4: V/F Control Parameters |
| P4.00 | V/F curve setting | 0：Linear V/F 1：Multi-point V/F 2：Square V/F 3：1.2-power V/F 4：1.4-power V/F 6：1.6-power V/F 8：1.8-power V/F 9：Reserved 10：V/F complete separation 11：V/F half separation | F400 | ★ |
| P4.01 | Torque boost | 0.0%：（fixed torque boost） 0.1%～30.0% | F401 | ☆ |
| P4.02 | Cut-off frequency of torque boost | 0.00Hz～maximum output frequency | F402 | ★ |
| P4.03 | Multi-point V/F frequency 1 (F1) | 0.00Hz～P4.05 | F403 | ★ |
| P4.04 | Multi-point V/F voltage 1 (V1) | 0.0%～100.0% | F404 | ★ |
| P4.05 | Multi-point V/F frequency 2 (F2) | P4.03～P4.07 | F405 | ★ |
| P4.06 | Multi-point V/F voltage 2 (V2) | 0.0%～100.0% | F406 | ★ |
| P4.07 | Multi-point V/F frequency 3 (F3) | P4.05～rated motor frequency （P1.04） | F407 | ★ |
| P4.08 | Multi-point V/F voltage 3 (V3) | 0.0%～100.0% | F408 | ★ |
| P4.09 | V/F slip compensation gain | 0.0%～200.0% | F409 | ☆ |
| P4.10 | V/F over-excitation gain | 0～200 | F40A | ☆ |
| P4.11 | V/F oscillation suppression gain | 0～100 | F40B | ☆ |
| P4.13 | Voltage source for V/F separation | 0：digital setting（P4.14） 1：FIV 2：FIC 3：Reserved 4：PULSE setting（S3） 5：Multi-reference 6：Simple PLC 7：PID 8：Communication setting 100.0% corresponds to the rated motor voltage. | F40D | ☆ |
| P4.14 | Voltage digital setting for V/F separation | 0V～rated motor voltage | F40E | ☆ |
| P4.15 | Voltage rise time of V/F separation | 0.0s～1000.0s It indicates the time for the voltage rising from 0 V to rated motor voltage. | F40F | ☆ |
| P4.16 | Voltage decline time of V/F separation | 0.0s～1000.0s It indicates the time for the voltage to decline from rated motor voltage to 0 V. | F410 | ☆ |
| Group P5: Input Terminals |
| P5.00 | FWD function selection | 0：No function 1：Forward RUN（FWD） 2：Reverse RUN（REV） 3：Three-line control 4：Forward JOG（FJOG） 5：Reverse JOG（RJOG） 6：Terminal UP 7：Terminal DOWN 8：Coast to stop 9：Fault reset（RESET） 10：RUN pause 11：Normally open (NO) input of external fault 12：Multi-reference terminal 1 13：Multi-reference terminal 2 14：Multi-reference terminal 3 15：Multi-reference terminal 4 16：Terminal 1 for acceleration/ deceleration time selection 17：Terminal 2 for acceleration/ deceleration time selection 18：Frequency source Switchover 19：UP and DOWN setting clear (terminal, operation panel) 20：Command source switchover terminal 21：Acceleration/Deceleration Prohibited 22：PID pause 23：PLC status reset 24：Swing pause 25：Counter input 26：Counter reset 27：Length count input 28：Length reset 29：Torque control prohibited 30：Pulse input （enabled only for S3） 31：Reserved 32：Immediate DC braking 33：Normally closed (NC) input of external fault 34：Frequency modification forbidden 35：Reverse PID action direction 36：External STOP terminal 1 37：Command source switchover terminal 2 38：PID integral pause 39：Switchover between main frequency source X and preset frequency 40：Switchover between auxiliary frequency source Y and preset frequency 41：Motor selection terminal 1 42：Motor selection terminal 2 43：PID parameter switchover 44：User-defined fault 1 45：User-defined fault 2 46：Speed control/Torque control switchover 47：Emergency stop 48：External STOP terminal 2 49：Deceleration DC braking 50：Clear the current running time 51-59:Reserved | F500 | ★ |
| P5.01 | REV function selection |  | F501 | ★ |
| P5.02 | S1 function selection |  | F502 | ★ |
| P5.03 | S2 function selection |  | F503 | ★ |
| P5.04 | S3 function selection |  | F504 | ★ |
| P5.05 | S4 function selection |  | F505 | ★ |
| P5.10 | S filter time | 0.000s～1.000s | F50A | ☆ |
| P5.11 | Terminal command mode | 0：Two-line mode 1 1：Two-line mode 2 2：Three-line mode 1 3：Three-line mode 2 | F50B | ★ |
| P5.12 | Terminal UP/DOWN rate | 0.001Hz/s～65.535Hz/s | F50C | ☆ |
| P5.13 | FI curve 1 minimum input | 0.00V～P5.15 | F50D | ☆ |
| P5.14 | Corresponding setting of FI curve 1 minimum input | -100.0%～+100.0% | F50E | ☆ |
| P5.15 | FI curve 1 maximum input | P5.13～+10.00V | F50F | ☆ |
| P5.16 | Corresponding setting of FI curve 1 maximum input | -100.0%～+100.0% | F510 | ☆ |
| P5.17 | FI curve 1 filter time | 0.00s～10.00s | F511 | ☆ |
| P5.18 | FI curve 2 minimum input | 0.00V～P5.20 | F512 | ☆ |
| P5.19 | Corresponding setting of FI curve 2 minimum input | -100.0%～+100.0% | F513 | ☆ |
| P5.20 | FI curve 2 maximum input | P5.18～+10.00V | F514 | ☆ |
| P5.21 | Corresponding setting of FI curve 2 maximum input | -100.0%～+100.0% | F515 | ☆ |
| P5.22 | FI curve 2 filter time | 0.00s～10.00s | F516 | ☆ |
| P5.23 | FI curve 3 minimum input | -10.00V～P5.25 | F517 | ☆ |
| P5.24 | Corresponding setting of FI curve 3 minimum input | -100.0%～+100.0% | F518 | ☆ |
| P5.25 | FI curve 3 maximum input | P5.23～+10.00V | F519 | ☆ |
| P5.26 | Corresponding setting of FI curve 3 maximum input | -100.0%～+100.0% | F51A | ☆ |
| P5.27 | FI curve 3 filter time | 0.00s～10.00s | F51B | ☆ |
| P5.28 | PULSE minimum input | 0.00kHz～P5.30 | F51C | ☆ |
| P5.29 | Corresponding setting of pulse minimum input | -100.0%～100.0% | F51D | ☆ |
| P5.30 | PULSE maximum input | P5.28～100.00kHz | F51E | ☆ |
| P5.31 | Corresponding setting of pulse maximum input | -100.0%～100.0% | F51F | ☆ |
| P5.32 | PULSE filter time | 0.00s～10.00s | F520 | ☆ |
| P5.33 | FI curve selection | Unit's digit：FIV curve selection 1：Curve 1（2 points, see P5.13～P5.16） 2：Curve 2（2 points, see P5.18～P5.21） 3：Curve 3（2 points, see P5.23～P5.26） 4：Curve 4（4 points, see C6.00～C6.07） 5：Curve 5（4 points, see C6.08～C6.15） Ten's digit：FIC curve selection（1～5，same as FIV） Hundred's digit：FIA curve selection（1～5，same as FIV） | F521 | ☆ |
| P5.34 | Setting for FI less than minimum input | Unit's digit:Setting for FIV less than minimum input 0:Minimum value 1:0.0% Ten's digit：Setting for FIC less than minimum input（0～1，same as FIV） Hundred's digit：Setting for FIA less than minimum input（0～1，same as FIV） | F522 | ☆ |
| P5.35 | FWD delay time | 0.0s～3600.0s | F523 | ★ |
| P5.36 | REV delay time | 0.0s～3600.0s | F524 | ★ |
| P5.37 | S1 delay time | 0.0s～3600.0s | F525 | ★ |
| P5.38 | S valid mode selection 1 | 0：High level valid 1：Low level valid Unit’s digit：FWD Ten’s digit：REV Hundred’s digit：S1 Thousand’s digit：S2 Ten thousand’s digit：S3 | F526 | ★ |
| P5.39 | S valid mode selection 2 | 0：High level valid 1：Low level valid Unit’s digit：S4 | F527 | ★ |
| Group P6: Output Terminals |
| P6.00 | M01 terminal output mode | 1：Switch signal output（M01） | F600 | ☆ |
| P6.01 | M01 function | 0：No output 1：AC drive running 2：Fault output (stop) 3：Frequency-level detection FDT1 output 4：Frequency reached 5：Zero-speed running(no output at stop) 6：Motor overload pre-warning 7：AC drive overload pre-warning 8：Set count value Reached 9：Designated count value reached 10：Length reached 11：PLC cycle complete 12：Accumulative running time reached 13：Frequency limited 14：Torque limited 15：Ready for RUN 16：FIV>FIC 17：Frequency upper limit reached 18：Frequency lower limit reached (no output at stop) 19：Under voltage state output 20：Communication setting 21：Reserved 22：Reserved 23：Zero-speed running 2 (having output at stop) 24：Accumulative power-on time reached 25：Frequency level detection FDT2 output 26：Frequency 1 reached 27：Frequency 2 reached 28：Current 1 reached 29：Current 2 reached 30：Timing reached 31：FIV input limit exceeded 32：Load becoming 0 33：Reverse running 34：Zero current state 35：Module temperature reached 36：Software current limit exceeded 37：Frequency lower limit reached (having output at stop) 38：Alarm output 39：Reserved 40：Current running time reached | F601 | ☆ |
| P6.02 | Relay output function（RA-RB-RC） |  | F602 | ☆ |
| P6.07 | FOV function selection | 0：Running frequency 1：Set frequency 2：Output current 3：Output torque 4：Output power 5：Output voltage 6：Pulse input（100.0% for 100.0kHz） 7：FIV 8：FIC 9：Reserved 10：Length 11：Count value 12：Communication setting 13：Motor rotational speed 14：Output current（100.0% for 1000.0A） 15：Output voltage（100.0% for 1000.0V） 16：Reserved | F607 | ☆ |
| P6.08 | Reserved |  | F608 |  |
| P6.09 | Reserved |  | F609 | ☆ |
| P6.10 | FOV offset coeffcient | -100.0%～+100.0% | F60A | ☆ |
| P6.11 | FOV gain | -10.00～+10.00 | F60B | ☆ |
| P6.12 | Reserved |  | F60C | ☆ |
| P6.13 | Reserved |  | F60D | ☆ |
| P6.17 | M01 output delay time | 0.0s～3600.0s | F611 | ☆ |
| P6.18 | RA-RB-RC output delay time | 0.0s～3600.0s | F612 | ☆ |
| P6.19 | Reserved |  | F613 | ☆ |
| P6.20 | Reserved |  | F614 | ☆ |
| P6.21 | Reserved |  | F615 | ☆ |
| P6.22 | Output terminal valid mode selection | 0：Positive logic 1：Negative logic Unit's digit：M01 Ten's digit：RA-RB-RC | F616 | ☆ |
| Group P7: Operation Panel and Display |
| P7.00 | Output power correction factor | 0.0-200.0 | F700 | ☆ |
| P7.01 | Reserved |  | F701 |  |
| P7.02 | STOP/RESET key function | 0:STOP/RESET key enabled only in operation panel control 1:STOP/RESET key enabled in any operation mode | F702 | ☆ |
| P7.03 | LED display running parameters 1 | 0000–FFFF Bit00: Running frequency 1 (Hz) Bit01: Set frequency (Hz) Bit02: Bus voltage (V) Bit03: Output voltage (V) Bit04: Output current (A) Bit05: Output power (kW) Bit06: Output torque (%) Bit07: S input status Bit08: M01 output status Bit09:FIV voltage (V) Bit10: FIC voltage (V) Bit11: Reserved Bit12: Count value Bit13: Length value Bit14: Load speed display Bit15: PID setting | F703 | ☆ |
| P7.04 | LED display running parameters 2 | 0000–FFFF Bit00: PID feedback Bit01: PLC stage Bit02: Pulse setting frequency(kHz) Bit03: Running frequency 2 (Hz) Bit04: Remaining running time Bit05: FIV voltage before correction (V) Bit06: FIC voltage before correction (V) Bit07: Reserved Bit08: Linear speed Bit09: Current power-on time(Hour) Bit10: Current running time (Min) Bit11: Pulse setting frequency(Hz) Bit12: Communication setting value Bit13: Reserved Bit14: Main frequency X display(Hz) Bit15:Auxiliary frequency Y display (Hz) | F704 | ☆ |
| P7.05 | LED display stop parameters | 0000–FFFF Bit00: Set frequency (Hz) Bit01: Bus voltage (V) Bit02: S input status Bit03: M01 output status Bit04: FIV voltage (V) Bit05: FIC voltage (V) Bit06: Reserved Bit07: Count value Bit08: Length value Bit09: PLC stage Bit10: Load speed Bit11: PID setting Bit12: Pulse setting frequency(kHz) | F705 | ☆ |
| P7.06 | Load speed display coeffcient | 0.0001～6.5000 | F706 | ☆ |
| P7.07 | Heatsink temperature of inverter | 0.0℃～100.0℃ | F707 | ● |
| P7.08 | Temporary software version | 0.0℃～100.0℃ | F708 | ● |
| P7.09 | Accumulative running time | 0h～65535h | F709 | ● |
| P7.10 | Reserved | - | F70A | ● |
| P7.11 | Software version | - | F70B | ● |
| P7.12 | Number of decimal places for load speed display | 0：0 decimal place 1：1 decimal place 2：2 decimal places 3：3 decimal places | F70C | ☆ |
| P7.13 | Accumulative power-on time | 0h～65535h | F70D | ● |
| P7.14 | Accumulative power consumption | 0kW～65535kWh | F70E | ● |
| Group P8: Auxiliary Functions |
| P8.00 | JOG running frequency | 0.00Hz～maximum frequency | F800 | ☆ |
| P8.01 | JOG acceleration time | 0.0s～6500.0s | F801 | ☆ |
| P8.02 | JOG deceleration time | 0.0s～6500.0s | F802 | ☆ |
| P8.03 | Acceleration time 2 | 0.0s～6500.0s | F803 | ☆ |
| P8.04 | Deceleration time 2 | 0.0s～6500.0s | F804 | ☆ |
| P8.05 | Acceleration time 3 | 0.0s～6500.0s | F805 | ☆ |
| P8.06 | Deceleration time 3 | 0.0s～6500.0s | F806 | ☆ |
| P8.07 | Acceleration time 4 | 0.0s～6500.0s | F807 | ☆ |
| P8.08 | Deceleration time 4 | 0.0s～6500.0s | F808 | ☆ |
| P8.09 | Jump frequency 1 | 0.00Hz～maximum frequency | F809 | ☆ |
| P8.10 | Jump frequency 2 | 0.00Hz～maximum frequency | F80A | ☆ |
| P8.11 | Frequency jump amplitude | 0.00Hz～maximum frequency | F80B | ☆ |
| P8.12 | Forward/Reverse rotation dead-zone time | 0.0s～3000.0s | F80C | ☆ |
| P8.13 | Reverse control | 0：Enabled 1：Disabled | F80D | ☆ |
| P8.14 | Running mode when set frequency lower than frequency lower limit | 0：Run at frequency lower limit 1：Stop 2：Run at zero speed | F80E | ☆ |
| P8.15 | Droop control | 0.00Hz～10.00Hz | F80F | ☆ |
| P8.16 | Accumulative power-on time threshold | 0h～65000h | F810 | ☆ |
| P8.17 | Accumulative running time threshold | 0h～65000h | F811 | ☆ |
| P8.18 | Startup protection | 0：No 1：Yes | F812 | ☆ |
| P8.19 | Frequency detection value（FDT1） | 0.00Hz～maximum frequency | F813 | ☆ |
| P8.20 | Frequency detection hysteresis（FDT1） | 0.0%～100.0%（FDT1 level） | F814 | ☆ |
| P8.21 | Detection range of frequency reached | 0.0%～100.0%（maximum frequency） | F815 | ☆ |
| P8.22 | Jump frequency during acceleration/ deceleration | 0：Disabled 1：Enabled | F816 | ☆ |
| P8.25 | Frequency switchover point between acceleration time 1 and acceleration time 2 | 0.00Hz～maximum frequency | F819 | ☆ |
| P8.26 | Frequency switchover point between deceleration time 1 and deceleration time 2 | 0.00Hz～maximum frequency | F81A | ☆ |
| P8.27 | Terminal JOG preferred | 0：Disabled 1：Enabled | F81B | ☆ |
| P8.28 | Frequency detection value (FDT2) | 0.00Hz～maximum frequency | F81C | ☆ |
| P8.29 | Frequency detection hysteresis (FDT2) | 0.0%～100.0%（FDT2 level） | F81D | ☆ |
| P8.30 | Any frequency reaching detection value 1 | 0.00Hz～maximum frequency | F81E | ☆ |
| P8.31 | Any frequency reaching detection amplitude 1 | 0.0%～100.0%（maximum frequency） | F81F | ☆ |
| P8.32 | Any frequency reaching detection value 2 | 0.00Hz～maximum frequency | F820 | ☆ |
| P8.33 | Any frequency reaching detection amplitude 2 | 0.0%～100.0%（maximum frequency） | F821 | ☆ |
| P8.34 | Zero current detection level | 0.0%～300.0% 100.0% for rated motor current | F822 | ☆ |
| P8.35 | Zero current detection delay time | 0.01s～600.00s | F823 | ☆ |
| P8.36 | Output over current threshold | 0.0%（no detection） 0.1%～300.0%（rated motor current） | F824 | ☆ |
| P8.37 | Output over current detection delay time | 0.00s～600.00s | F825 | ☆ |
| P8.38 | Any current reaching 1 | 0.0%～300.0%（rated motor current） | F826 | ☆ |
| P8.39 | Any current reaching 1 amplitude | 0.0%～300.0%（rated motor current） | F827 | ☆ |
| P8.40 | Any current reaching 2 | 0.0%～300.0%（rated motor current） | F828 | ☆ |
| P8.41 | Any current reaching 2 amplitude | 0.0%～300.0%（rated motor current） | F829 | ☆ |
| P8.42 | Timing function | 0:Disabled 1:Enabled | F82A | ☆ |
| P8.43 | Timing duration source | 0：P8.44 1：FIV 2：FIC 100% of analog input corresponds to the value of P8.44 | F82B | ☆ |
| P8.44 | Timing duration | 0.0Min～6500.0Min | F82C | ☆ |
| P8.45 | FIV input voltage lower limit | 0.00V～P8.46 | F82D | ☆ |
| P8.46 | FIV input voltage upper limit | P8.45～10.00V | F82E | ☆ |
| P8.47 | Module temperature threshold | 0℃～150℃ | F82F | ☆ |
| P8.48 | Cooling fan control | 0：Fan working during running 1：Fan working continuously | F830 | ☆ |
| P8.49 | Wakeup frequency | Dormant frequency（P8.51）～maximum frequency（P0.12） | F831 | ☆ |
| P8.50 | Wakeup delay time | 0.0s～6500.0s | F832 | ☆ |
| P8.51 | Dormant frequency | 0.00Hz～wakeup frequency（P8.49） | F833 | ☆ |
| P8.52 | Dormant delay time | 0.0s～6500.0s | F834 | ☆ |
| P8.53 | Current running time reached | 0.0Min～6500.0Min | F835 | ☆ |
| Group P9: Fault and Protection |
| P9.00 | Motor overload protection selection | 0：Disabled 1：Enabled | F900 | ☆ |
| P9.01 | Motor overload protection gain | 0.20～10.00 | F901 | ☆ |
| P9.02 | Motor overload warning coeffcient | 50%～100% | F902 | ☆ |
| P9.03 | Overvoltage stall gain | 0～100 | F903 | ☆ |
| P9.04 | Overvoltage stall protective voltage | 120%～150% | F904 | ☆ |
| P9.05 | Over current stall gain | 0～100 | F905 | ☆ |
| P9.06 | Over current stall protective current | 100%～200% | F906 | ☆ |
| P9.07 | Short-circuit to ground upon power-on | 0：Disabled 1：Enabled | F907 | ☆ |
| P9.09 | Fault auto reset times | 0～20 | F909 | ☆ |
| P9.10 | M01 action during fault auto reset | 0：Not act 1：Act | F90A | ☆ |
| P9.11 | Time interval of fault auto reset | 0.1s～100.0s | F90B | ☆ |
| P9.12 | Reserved |  | F90C | ☆ |
| P9.13 | Output phase loss protection selection | 0：Disabled 1：Enabled | F90D | ☆ |
| P9.14 | 1st fault type | 0: No fault 1: Inverter unit protection 2: Overcurrent during acceleration 3: Overcurrent during deceleration 4: Overcurrent at constant speed 5: Overvoltage during acceleration 6: Overvoltage during deceleration 7: Overvoltage at constant speed 8: Buffer resistance overload 9: Undervoltage 10: AC drive overload 11: Motor overload 12:Reserved 13: Power output phase loss 14: Module overheat 15: External equipment fault 16: Communication fault 17: Contactor fault 18: Current detection fault 19: Motor auto-tuning fault 20: Reserved 21: EEPROM read-write fault 22: AC drive hardware fault 23: Short circuit to ground 24: Reserved 25: Reserved 26:Accumulative running time reached 27: Reserved 28: Reserved 29: Accumulative power-on time reached 30: Load becoming 0 31: PID feedback lost during running 40: With-wave current limit fault 41-43: Reserved 51: Reserved | F90E | ● |
| P9.15 | 2nd fault type |  | F90F | ● |
| P9.16 | 3rd (latest) fault type |  | F910 | ● |
| P9.17 | Frequency upon 3rd fault | － | F911 | ● |
| P9.18 | Current upon 3rd fault | － | F912 | ● |
| P9.19 | Bus voltage upon 3rd fault | － | F913 | ● |
| P9.20 | Input terminal status upon 3rd fault | － | F914 | ● |
| P9.21 | Output terminal status upon 3rd fault | － | F915 | ● |
| P9.22 | AC drive status upon 3rd fault | － | F916 | ● |
| P9.23 | Power-on time upon 3rd fault | － | F917 | ● |
| P9.24 | Running time upon 3rd fault | － | F918 | ● |
| P9.27 | Frequency upon 2nd fault | － | F91B | ● |
| P9.28 | Current upon 2nd fault | － | F91C | ● |
| P9.29 | Bus voltage upon 2nd fault | － | F91D | ● |
| P9.30 | Iutput terminal status upon 2nd fault | － | F91E | ● |
| P9.31 | Output terminal status upon 2nd fault | － | F91F | ● |
| P9.32 | Frequency upon 2nd fault | － | F920 | ● |
| P9.33 | Current upon 2nd fault | － | F921 | ● |
| P9.34 | Bus voltage upon 2nd fault | － | F922 | ● |
| P9.37 | Iutput terminal status upon 1st fault | － | F925 | ● |
| P9.38 | Output terminal status upon 1st fault | － | F926 | ● |
| P9.39 | Frequency upon 1st fault | － | F927 | ● |
| P9.40 | Current upon 1st fault | － | F928 | ● |
| P9.41 | Bus voltage upon 3rd fault | － | F929 | ● |
| P9.42 | Iutput terminal status upon 1st fault | － | F92A | ● |
| P9.43 | Output terminal status upon 1st fault | － | F92B | ● |
| P9.44 | Frequency upon 1st fault | － | F92C | ● |
| P9.47 | Fault protection action selection 1 | Unit's digit：Motor overload（OL1） 0：Coast to stop 1：Stop according to the stop mode 2：Continue to run Ten's digit：Power input phase loss（LI） Hundred's digit：Power output phase loss（LO） Thousand's digit：External equipment fault（EF） Ten thousand's digit：Communication fault（CE） | F92F | ☆ |
| P9.48 | Fault protection action selection 2 | Unit's digit：Reserved 0：Coast to stop Ten's digit：EEPROM read-write fault（EEP） 0：Coast to stop 1：Stop according to the stop mode Hundred's digit：Reserved Thousand's digit：Reserved Ten thousand's digit：Accumulative running time reached（END1） | F930 | ☆ |
| P9.49 | Fault protection action selection 3 | Unit's digit：Reserved 0：Coast to stop 1：Stop according to the stop mode 2：Continue to run Ten's digit：Reserved 0：Coast to stop 1：Stop according to the stop mode 2：Continue to run Hundred's digit：Accumulative power-on time reached（END2） 0：Coast to stop 1：Stop according to the stop mode 2：Continue to run Thousand's digit：Load becoming 0 0：Coast to stop 1：Stop according to the stop mode 2：Continue to run at 7% of rated motor frequency and resume to the set frequency if the load recovers Ten thousand's digit： PID feedback loss of running 0：Coast to stop 1：Stop according to the stop mode 2：Continue to run | F931 | ☆ |
| P9.50 | Reserved |  | F932 | ☆ |
| P9.54 | Frequency selection for continuing to run | 0：Current running frequency 1：Set frequency 2：Frequency upper limit 3：Frequency lower limit 4：Backup frequency upon abnormality | F936 | ☆ |
| P9.55 | Backup frequency upon abnormality | 60.0%～100.0% | F937 | ☆ |
| P9.56 | reserved |  | F938 | ☆ |
| P9.57 | reserved |  | F939 | ☆ |
| P9.58 | reserved |  | F93A | ☆ |
| P9.59 | Action selection at instantaneous power failure | 0：Invalid 1：Decelerate 2：Decelerate to stop | F93B | ☆ |
| P9.60 | Action pause judging voltage at instantaneous power failure | 0.0%～100.0% | F93C | ☆ |
| P9.61 | Voltage rally judging time at instantaneous power failure | 0.00s～100.00s | F93D | ☆ |
| P9.62 | Action judging voltage at instantaneous power failure | 60.0%～100.0%（standard bus voltage） | F93E | ☆ |
| P9.63 | Protection upon load becoming 0 | 0：Disabled 1：Enabled | F93F | ☆ |
| P9.64 | Detection level of load becoming 0 | 0.0～100.0％ | F940 | ☆ |
| P9.65 | Detection time of load becoming 0 | 0.0～60.0s | F941 | ☆ |
| P9.67 | Reserved |  | F943 | ☆ |
| P9.68 | Reserved |  | F944 | ☆ |
| P9.69 | Reserved |  | F945 | ☆ |
| P9.70 | Reserved |  | F946 | ☆ |
| Group PA: Process Control PID Function |
| PA.00 | PID setting source | 0：PA.01 1：FIV 2：FIC 3：Reserved 4：PULSE setting（S3） 5：Communication setting 6：Multi-reference | FA00 | ☆ |
| PA.01 | PID digital setting | 0.0%～100.0% | FA01 | ☆ |
| PA.02 | PID feedback source | 0：FIV 1：FIC 2：Reserved 3：FIV-FIC 4：PULSE setting（S3） 5：Communication setting 6：FIV+FIC 7：MAX（¦FIV¦, ¦FIC¦） 8：MIN（¦FIV¦, ¦FIC¦） | FA02 | ☆ |
| PA.03 | PID action direction | 0：Forward action 1：Reverse action | FA03 | ☆ |
| PA.04 | PID setting feedback range | 0～65535 | FA04 | ☆ |
| PA.05 | Proportional gain Kp1 | 0.0～100.0 | FA05 | ☆ |
| PA.06 | Integral time Ti1 | 0.01s～10.00s | FA06 | ☆ |
| PA.07 | Differential time Td1 | 0.000s～10.000s | FA07 | ☆ |
| PA.08 | Cut-off frequency of PID reverse rotation | 0.00～maximum frequency | FA08 | ☆ |
| PA.09 | PID deviation limit | 0.0%～100.0% | FA09 | ☆ |
| PA.10 | PID differential limit | 0.00%～100.00% | FA0A | ☆ |
| PA.11 | PID setting change time | 0.00～650.00s | FA0B | ☆ |
| PA.12 | PID feedback filter time | 0.00～60.00s | FA0C | ☆ |
| PA.13 | PID output filter time | 0.00～60.00s | FA0D | ☆ |
| PA.14 | Reserved | - | FA0E | ☆ |
| PA.15 | Proportional gain Kp2 | 0.0～100.0 | FA0F | ☆ |
| PA.16 | Integral time Ti2 | 0.01s～10.00s | FA10 | ☆ |
| PA.17 | Differential time Td2 | 0.000s～10.000s | FA11 | ☆ |
| PA.18 | PID parameter switchover condition | 0：No switchover 1：Switchover via S 2：Automatic switchover based on deviation | FA12 | ☆ |
| PA.19 | PID parameter switchover deviation 1 | 0.0%～PA.20 | FA13 | ☆ |
| PA.20 | PID parameter switchover deviation 2 | PA.19～100.0% | FA14 | ☆ |
| PA.21 | PID initial value | 0.0%～100.0% | FA15 | ☆ |
| PA.22 | PID initial value holding time | 0.00～650.00s | FA16 | ☆ |
| PA.23 | Maximum deviation between two PID outputs in forward | 0.00%～100.00% | FA17 | ☆ |
| PA.24 | Maximum deviation between two PID outputs in reverse | 0.00%～100.00% | FA18 | ☆ |
| PA.25 | PID integral property | Unit's digit：Integral separated 0：Invalid 1：Valid Ten's digit：Whether to stop integral operation when the output reaches 0：Continue integral operation 1：Stop integral operation | FA19 | ☆ |
| PA.26 | Detection value of PID feedback loss | 0.0%：Not judging feedback loss 0.1%～100.0％ | FA1A | ☆ |
| PA.27 | Detection time of PID feedback loss | 0.0s～20.0s | FA1B | ☆ |
| PA.28 | PID operation at stop | 0：No PID operation at stop 1：PID operation at stop | FA1C | ☆ |
| Group Pb: Swing Frequency, Fixed Length and Count |
| Pb.00 | Swing frequency setting mode | 0：Relative to the central frequency 1：Relative to the maximum frequency | FB00 | ☆ |
| Pb.01 | Swing frequency amplitude | 0.0%～100.0% | FB01 | ☆ |
| Pb.02 | Jump frequency amplitude | 0.0%～50.0% | FB02 | ☆ |
| Pb.03 | Swing frequency cycle | 0.1s～3000.0s | FB03 | ☆ |
| Pb.04 | Triangular wave rising time coefficient | 0.1%～100.0% | FB04 | ☆ |
| Pb.05 | Set length | 0m～65535m | FB05 | ☆ |
| Pb.06 | Actual length | 0m～65535m | FB06 | ☆ |
| Pb.07 | Number of pulses per meter | 0.1～6553.5 | FB07 | ☆ |
| Pb.08 | Set count value | 1～65535 | FB08 | ☆ |
| Pb.09 | Designated count value | 1～65535 | FB09 | ☆ |
| Group PC: Multi-Reference and Simple PLC Function |
| PC.00 | Reference 0 | -100.0%～100.0% | FC00 | ☆ |
| PC.01 | Reference 1 | -100.0%～100.0% | FC01 | ☆ |
| PC.02 | Reference 2 | -100.0%～100.0% | FC02 | ☆ |
| PC.03 | Reference 3 | -100.0%～100.0% | FC03 | ☆ |
| PC.04 | Reference 4 | -100.0%～100.0% | FC04 | ☆ |
| PC.05 | Reference 5 | -100.0%～100.0% | FC05 | ☆ |
| PC.06 | Reference 6 | -100.0%～100.0% | FC06 | ☆ |
| PC.07 | Reference 7 | -100.0%～100.0% | FC07 | ☆ |
| PC.08 | Reference 8 | -100.0%～100.0% | FC08 | ☆ |
| PC.09 | Reference 9 | -100.0%～100.0% | FC09 | ☆ |
| PC.10 | Reference10 | -100.0%～100.0% | FC0A | ☆ |
| PC.11 | Reference11 | -100.0%～100.0% | FC0B | ☆ |
| PC.12 | Reference12 | -100.0%～100.0% | FC0C | ☆ |
| PC.13 | Reference13 | -100.0%～100.0% | FC0D | ☆ |
| PC.14 | Reference14 | -100.0%～100.0% | FC0E | ☆ |
| PC.15 | Reference15 | -100.0%～100.0% | FC0F | ☆ |
| PC.16 | Simple PLC running mode | 0：Stop after the AC drive runs one cycle 1：Keep final values after the AC drive runs one cycle 2：Repeat after the AC drive runs one cycle | FC10 | ☆ |
| PC.17 | Simple PLC retentive selection | Unit's digit：Retentive upon power failure 0：No 1：Yes Ten's digit：Retentive upon stop 0：No 1：Yes | FC11 | ☆ |
| PC.18 | Running time of simple PLC reference 0 | 0.0s（h）～6553.5s（h） | FC12 | ☆ |
| PC.19 | Acceleration/deceleration time of simple PLC reference 0 | 0～3 | FC13 | ☆ |
| PC.20 | Running time of simple PLC reference 1 | 0.0s（h）～6553.5s（h） | FC14 | ☆ |
| PC.21 | Acceleration/deceleration time of simple PLC reference 1 | 0～3 | FC15 | ☆ |
| PC.22 | Running time of simple PLC reference 2 | 0.0s（h）～6553.5s（h） | FC16 | ☆ |
| PC.23 | Acceleration/deceleration time of simple PLC reference 2 | 0～3 | FC17 | ☆ |
| PC.24 | Running time of simple PLC reference 3 | 0.0s（h）～6553.5s（h） | FC18 | ☆ |
| PC.25 | Acceleration/deceleration time of simple PLC reference 3 | 0～3 | FC19 | ☆ |
| PC.26 | Running time of simple PLC reference 4 | 0.0s（h）～6553.5s（h） | FC1A | ☆ |
| PC.27 | Acceleration/deceleration time of simple PLC reference 4 | 0～3 | FC1B | ☆ |
| PC.28 | Running time of simple PLC reference 5 | 0.0s（h）～6553.5s（h） | FC1C | ☆ |
| PC.29 | Acceleration/deceleration time of simple PLC reference 5 | 0～3 | FC1D | ☆ |
| PC.30 | Running time of simple PLC reference 6 | 0.0s（h）～6553.5s（h） | FC1E | ☆ |
| PC.31 | Acceleration/deceleration time of simple PLC reference 6 | 0～3 | FC1F | ☆ |
| PC.32 | Running time of simple PLC reference 7 | 0.0s（h）～6553.5s（h） | FC20 | ☆ |
| PC.33 | Acceleration/deceleration time of simple PLC reference 7 | 0～3 | FC21 | ☆ |
| PC.34 | Running time of simple PLC reference 8 | 0.0s（h）～6553.5s（h） | FC22 | ☆ |
| PC.35 | Acceleration/deceleration time of simple PLC reference 8 | 0～3 | FC23 | ☆ |
| PC.36 | Running time of simple PLC reference 9 | 0.0s（h）～6553.5s（h） | FC24 | ☆ |
| PC.37 | Acceleration/deceleration time of simple PLC reference 9 | 0～3 | FC25 | ☆ |
| PC.38 | Running time of simple PLC reference 10 | 0.0s（h）～6553.5s（h） | FC26 | ☆ |
| PC.39 | Acceleration/deceleration time of simple PLC reference 10 | 0～3 | FC27 | ☆ |
| PC.40 | Running time of simple PLC reference 11 | 0.0s（h）～6553.5s（h） | FC28 | ☆ |
| PC.41 | Acceleration/deceleration time of simple PLC reference 11 | 0～3 | FC29 | ☆ |
| PC.42 | Running time of simple PLC reference 12 | 0.0s（h）～6553.5s（h） | FC2A | ☆ |
| PC.43 | Acceleration/deceleration time of simple PLC reference 12 | 0～3 | FC2B | ☆ |
| PC.44 | Running time of simple PLC reference 13 | 0.0s（h）～6553.5s（h） | FC2C | ☆ |
| PC.45 | Acceleration/deceleration time of simple PLC reference 13 | 0～3 | FC2D | ☆ |
| PC.46 | Running time of simple PLC reference 14 | 0.0s（h）～6553.5s（h） | FC2E | ☆ |
| PC.47 | Acceleration/deceleration time of simple PLC reference 14 | 0～3 | FC2F | ☆ |
| PC.48 | Running time of simple PLC reference 15 | 0.0s（h）～6553.5s（h） | FC30 | ☆ |
| PC.49 | Acceleration/deceleration time of simple PLC reference 15 | 0～3 | FC31 | ☆ |
| PC.50 | Time unit of simple PLC running | 0：s（second） 1：h（hour） | FC32 | ☆ |
| PC.51 | Reference 0 source | 0：Set by PC.00 1：FIV 2：FIC 3：Reserved 4：PULSE setting 5：PID Set by preset frequency (P0.10), modified via terminal UP/DOWN | FC33 | ☆ |
| Group PE: Reserved |
| Group PP: User-Defined Function Codes |
| PP.00 | User password | 0～65535 | - | ☆ |
| PP.01 | Restore default settings | 0：No operation 01：Restore factory settings except motor parameters 02：Clear records 04：Restore user backup parameters 501：Back up current user parameters | - | ★ |
| Group C0: Torque Control and Restricting Parameters |
| C0.00 | Speed/Torque control selection | 0：Speed control 1：Torque control | A000 | ★ |
| C0.01 | Torque setting source in torque control | 0：Digital setting（C0.03） 1：FIV 2：FIC 3：Reserved 4：PULSE setting 5：Communication setting 6：MIN（FIV,FIC） 7：MAX（FIV,FIC） | A001 | ★ |
| C0.03 | Torque digital setting in torque control数字设定 | -200.0%～200.0% | A003 | ☆ |
| C0.05 | Forward maximum frequency in torque control | 0.00Hz～maximum frequency | A005 | ☆ |
| C0.06 | Reverse maximum frequency in torque control | 0.00Hz～maximum frequency | A006 | ☆ |
| C0.07 | Acceleration time in torque control | 0.00s～65000s | A007 | ☆ |
| C0.08 | Deceleration time in torque control | 0.00s～65000s | A008 | ☆ |
| Group C1-C4: Reserved |
| Group C5: Control Optimization Parameters |
| C5.00 | PWM switchover frequency upper limit | 0.00Hz～15.00Hz | A500 | ☆ |
| C5.01 | PWM modulation mode | 0: Asynchronous modulation 1: Synchronous modulation | A501 | ☆ |
| C5.02 | Dead zone compensation mode selection | 0: No compensation 1: Compensation mode 1 2: Compensation mode 2 | A502 | ☆ |
| C5.03 | Random PWM depth | 0: Random PWM invalid 1–10:PWM carrier frequency random depth | A503 | ☆ |
| C5.04 | Rapid current limit | 0: Disabled 1: Enabled | A504 | ☆ |
| C5.05 | Current detection compensation | 0～100 | A505 | ☆ |
| C5.06 | Undervoltage threshold | 60.0%～140.0% | A506 | ☆ |
| C5.07 | SFVC optimization mode selection | 0：No optimization 1：Optimization mode 1 2：Optimization mode 2 | A507 | ☆ |
| Group C6: FI Curve Setting(FI is FIV or FIC) |
| C6.00 | FI curve 4 minimum input | -10.00V～C6.02 | A600 | ☆ |
| C6.01 | Corresponding setting of FI curve 4 minimum input | -100.0%～+100.0% | A601 | ☆ |
| C6.02 | FI curve 4 inflexion 1 input | C6.00～C6.04 | A602 | ☆ |
| C6.03 | Corresponding setting of FI curve 4 inflexion 1 input | -100.0%～+100.0% | A603 | ☆ |
| C6.04 | FI curve 4 inflexion 2 input | C6.02～C6.06 | A604 | ☆ |
| C6.05 | Corresponding setting of FI curve 4 inflexion 2 input | -100.0%～+100.0% | A605 | ☆ |
| C6.06 | FI curve 4 maximum input | C6.06～+10.00V | A606 | ☆ |
| C6.07 | Corresponding setting of FI curve 4 maximum input | -100.0%～+100.0% | A607 | ☆ |
| C6.08 | FI curve 5 minimum input | -10.00V～C6.10 | A608 | ☆ |
| C6.09 | Corresponding setting of FI curve 5 minimum input | -100.0%～+100.0% | A609 | ☆ |
| C6.10 | FI curve 5 inflexion 1 input | C6.08～C6.12 | A60A | ☆ |
| C6.11 | Corresponding setting of FI curve 5 inflexion 1 input | -100.0%～+100.0% | A60B | ☆ |
| C6.12 | FI curve 5 inflexion 2 input | C6.10～C6.14 | A60C | ☆ |
| C6.13 | Corresponding setting of FI curve 5 inflexion 2 input | -100.0%～+100.0% | A60D | ☆ |
| C6.14 | FI curve 5 maximum input | C6.12～+10.00V | A60E | ☆ |
| C6.15 | Corresponding setting of FI curve 5 maximum input | -100.0%～+100.0% | A60F | ☆ |
| C6.16 | Jump point of FIV input corresponding setting | -100.0%～100.0% | A610 | ☆ |
| C6.17 | Jump amplitude of FIV input corresponding setting | 0.0%～100.0% | A611 | ☆ |
| C6.18 | Jump point of FIC input corresponding setting | -100.0%～100.0% | A612 | ☆ |
| C6.19 | Jump amplitude of FIC input | 0.0%～100.0% | A613 | ☆ |
| Group CC: FI/FO Correction |
| CC.00 | FIV measured voltage 1 | 0.500V～4.000V | AC00 | ☆ |
| CC.01 | FIV displayed voltage 1 | 0.500V～4.000V | AC01 | ☆ |
| CC.02 | FIV measured voltage 2 | 6.000V～9.999V | AC02 | ☆ |
| CC.03 | FIV displayed voltage 2 | 6.000V～9.999V | AC03 | ☆ |
| CC.04 | FIC measured voltage 1 | 0.500V～4.000V | AC04 | ☆ |
| CC.05 | FIC displayed voltage 1 | 0.500V～4.000V | AC05 | ☆ |
| CC.06 | FIC measured voltage 2 | 6.000V～9.999V | AC06 | ☆ |
| CC.07 | FIC displayed voltage 2 | 6.000V～9.999V | AC07 | ☆ |
| CC.08 | Reserved |  | AC08 | ☆ |
| CC.09 | Reserved |  | AC09 | ☆ |
| CC.10 | Reserved |  | AC0A | ☆ |
| CC.11 | Reserved |  | AC0B | ☆ |
| CC.12 | FOV target voltage 1 | 0.500V～4.000V | AC0C | ☆ |
| CC.13 | FOV measured voltage 1 | 0.500V～4.000V | AC0D | ☆ |
| CC.14 | FOV target voltage 2 | 6.000V～9.999V | AC0E | ☆ |
| CC.15 | FOV measured voltage 2 | 6.000V～9.999V | AC0F | ☆ |
| CC.16 | Reserved |  | AC10 | ☆ |
| CC.17 | Reserved |  | AC11 | ☆ |
| CC.18 | Reserved |  | AC12 | ☆ |
| CC.19 | Reserved |  | AC13 | ☆ |

Group D0: Monitoring Parameters

| Function Code | Parameter Name | Command address | Unit |
| --- | --- | --- | --- |
| D0.00 | Running frequency（Hz） | 7000 | 0.01Hz |
| D0.01 | Set frequency（Hz） | 7001 | 0.01Hz |
| D0.02 | Bus voltage（V） | 7002 | 0.1V |
| D0.03 | Bus voltage（V） | 7003 | 1V |
| D0.04 | Output current（A） | 7004 | 0.01A |
| D0.05 | Output power（kW） | 7005 | 0.1kW |
| D0.06 | Output torque（%） | 7006 | 0.1% |
| D0.07 | S input state | 7007 | 1 |
| D0.08 | M01 output state | 7008 | 1 |
| D0.09 | FIV voltage（V） | 7009 | 0.01V |
| D0.10 | FIC voltage（V） | 700A | 0.01V |
| D0.11 | Reserved | 700B |  |
| D0.12 | Count value | 700C | 1 |
| D0.13 | Length | 700D | 1 |
| D0.14 | Load speed | 700E | 1 |
| D0.15 | PID setting | 700F | 1 |
| D0.16 | PID feedback | 7010 | 1 |
| D0.17 | PLCstage | 7011 | 1 |
| D0.18 | Input pulse frequency | 7012 | 0.01kHz |
| D0.19 | Reserved | 7013 |  |
| D0.20 | Remaining running time | 7014 | 0.1Min |
| D0.21 | FIV voltage before correction | 7015 | 0.001V |
| D0.22 | FIC voltage before correction | 7016 | 0.001V |
| D0.23 | Reserved | 7017 |  |
| D0.24 | Linear speed | 7018 | 1m/Min |
| D0.25 | On the current time | 7019 | 1Min |
| D0.26 | The current running time | 701A | 0.1Min |
| D0.27 | Pulse input frequency | 701B | 1Hz |
| D0.28 | Communication setting value | 701C | 0.01% |
| D0.29 | Reserved | 701D |  |
| D0.30 | Reserved | 701E |  |
| D0.31 | Auxiliary frequency Y | 701F | 0.01Hz |
| D0.32 | View any memory address values | 7020 | 1 |
| D0.33 | Reserved | 7021 |  |
| D0.34 | Motor temperature | 7022 | 1℃ |
| D0.35 | Target torque | 7023 | 0.1% |
| D0.36 | Reserved | 7024 |  |
| D0.37 | Power factor angle | 7025 | 0.1 |
| D0.38 | Reserved | 7026 |  |
| D0.39 | Target voltage upon V/F separation | 7027 | 1V |
| D0.40 | Output voltage upon V/F separation | 7028 | 1V |
| D0.41 | Reserved | 7029 |  |
| D0.42 | Reserved | 702A |  |
| D0.43 | Reserved | 702B |  |
| D0.44 | Reserved | 702C |  |
| D0.45 | Current fault code | 702D | 0 |